## Slide 1: Coke Oven Gas Main (COGM)
Decontamination Project

## Slide 2
RCO
SBCO
N
Steel house
RSP
RBF
RPS
c. 8 k Arterial
RCO > < SBCO
N2 imported into the COG system at this point from BOC
c. 3 k Arterial
Underground
TLRS
British Steel & TATA
c. 2 k Elevated & c. 3 k Underground
Tata & British Steel
c. 1.7 k
SBCO - TLRS
c. 2.5 k
SBCO
c. 2.5 k
RCO
c. 4 k Arterial
RSP-RPS-RBF
STSC COGM Decontamination project

## Slide 3
c. 6 K
c. 2K
N2 imported
from BOC
RCO
SBCO
STSC COGM P&ID
SBCO to RCO c. 600mm Diameter COG arterial main (c3Km buried underground sections at a depth of c. 2.5m)

## Slide 4
c. 6 K
c. 2K
N2 imported
from BOC
RCO
SBCO
STSC COGM Annotated P&ID

## Slide 5
S.T.S.C. Coke Oven Gas [COG] Decontamination project
SBV2
SBV16
SBCO
TLRS
SBV7
COV7

## Slide 6
A pyrophoric substance is one which will ignite
spontaneously in air at or below 55OC without
an ignition source being required.
Various examples of COGM
contaminant deposits & pyrophoric
material in the mains
Solid COGM deposits consist mainly Naphthalene (flammable)
600mm dia Arterial COGM
600mm dia Arterial COGM
1200mm dia SBCO COGM
1200mm dia SBCO COGM
STSC COGM - 2014 Wash Out

## Slide 7
Before washout
Before washout
During washout
During washout
After washout
STSC COGM – 2015 SBCO By Products Wash Out

## Slide 8
Partially dug excavation with clay pipe fitted above DP 88 siphon pot
Exposed siphon pot DP88 with stainless steel drain leg
Stone like crust on DP 88 siphon pot
Completed excavation with above DP 88 siphon pot
600mm dia underground arterial COGM
STSC COGM – Excavated Inspection of 2014

## Slide 9
Calculation for estimating quantity of residue within COG mains
pi x radius squared x Length
1 metre length of 600 mm dia arterial COG Main
3.14159265 x 0.32 x 1m = 0.2827 m3
V = π x r2 x L
STSC COGM Quantity of Residue

## Slide 10
Assume COG mains contain 50% residue with an S.G. of 1.0
Volume of COG residue in a 1 m length of 600 mm dia main: 0.2827 m3 / 50%
Volume of 1 metre length of 600 mm dia COG main = 0.2827 m3
0.1413 m3
STSC COGM Quantity of Residue
Calculation for estimating quantity of residue within COG mains