PART TWO

SPECIFICATION

PREAMBLE

General Requirements

Tenders are invited from Kettering Borough Council for the refurbishment of the chapel at Rothwell Town Cemetery, Loddington Road, Rothwell, Northamptonshire NN14 1RX.

Information, Costs and Expenses

Contractors are responsible for obtaining all information necessary for the preparation of their Quotation and all costs expenses and liabilities incurred in connection with the preparation and submission of a quotation.

Submission of Quotation

Your quotation should be submitted together with any Pricing Schedule and Supporting Information to:

webprocurement@kettering.gov.uk.

Further information and Queries

Please address any queries or requests for further information to:

webprocurement@kettering.gov.uk

Freedom of Information Act 2000:

  - Information in relation to this tender may be made available on demand in accordance with the requirements of the Freedom of Information Act 2000.

  - Contractors should state if any of the information supplied by them is confidential or commercially sensitive or should not be disclosed in response to a request for information under the Act.  Contractors should state why they consider the information to be confidential or commercially sensitive.  This will not guarantee that the information will not be disclosed but will be examined in the light of the exemptions provided in the Act.

  - It is important to note that information may be commercially sensitive for a time (e.g. during a tender process) but afterwards it may not be.  The timing of any request for information may be extremely important in determining whether information is exempt.  However, contactors should note that no information is likely to be regarded as exempt forever.

SPECIFICATION

Introduction and Context

The current chapel is in a poor state of repair and is well below current construction standards. The intention is to undertake all the essential repairs to the chapel to maintain its structural integrity and improve its current condition such that further works are not required for a minimum of 5 years. When the work is being executed the successful contractor shall ensure that all areas of the cemetery can be regularly used by funeral directors, visiting public and maintenance contractors.

Core Works

Refurbish roof by installing new breather felt and Flashings, replace existing floor, repair / replace internal finishes and install secondary glazing and install a surface water drain if funds allow to improve the existing Chapel at Rothwell Town Cemetery, Loddington Road, Rothwell, Northamptonshire NN14 1RX.

It is intended to improve the condition of the chapel by:

- Clearing Shrubs and removing soil to a minimum of 300mm below Floor level.

- Erecting Scaffolding to undertake roof works and removal on completion of works.

- Executing roofing works including installation of new breather felt on new treated battens with replacement Lead Flashing.

- Repairing or replacing any rotten Roof timbers.

- Repairing Bell Tower.

- Renewing rainwater goods and Fascia.

- Repairing and Repointing external Brickwork and Parapet coping.

- Supplying and installing hardcore, permeable infill finish and drainage Channels around building to divert rainwater from walls.

- Breaking up existing floors and install new insulated floor with D.P.M and a minimum of 75mm depth of screed.

- Removing Dado rails and all plaster to walls, injecting a chemical DPC and tanking to walls, Dry lining walls, plaster and skimming lining, installing new skirting boards and Dado rails.

- Easing, fitting new hinges and rehanging all internal and external doors.

- Installing secondary double glazing and making repairs to existing glazing

- Upgrading Electrical system to current standards.

- Completely decorating internal walls, all doors and Rainwater goods to protect completed works.

- Install a Yard Gulley to take water from the drainage into the existing land drain adjacent to the Loddington Road pedestrian access to the cemetery via a 100mm dia. Drain if funds allow.

It is envisaged that there will be a minimum of excavation and it should be noted that all the excavated material should be removed from site and properly disposed of.

The area available for construction of the works is the whole of the Cemetery as defined by distinct fenced boundaries, clearly visible on site. Contractors should indicate the intended sites for storage of materials when submitting their tender.

Contractors should indicate the measures that they will take to allow any funerals to be undertaken and the period for which they are likely to be on site.

Responsibilities

The Pubic Services Team is responsible for the maintenance of the grounds, including the excavation of graves, any allocation of plots that maybe required and for these works being executed.

Use of Site

Rothwell Town Cemetery is still in use and there is an average of two funeral service per month held at the site. Funeral and Internment of Ashes services are carried out within the cemetery and Contractors should ensure that the site is as clear as is possible of construction materials, plant and staff whilst any services are being executed.

The Bereavement Services Section of the Council will give a minimum of 7 day’s notice of any funeral or other service at Rothwell Town Cemetery to the Project Manager who will notify the successful tenderer during the time of the execution of the work.

OUTLINE SPECIFICATION FOR WORKS AT ROTHWELL TOWN CEMETERY

Site Clearance

Clear all shrubs and planting around the chapel and excavate to allow installation of permeable surfacing and drainage to the building.

External Works

Install dished concrete drainage channel with kerb upstand to rear and both sides of building to divert water away from the building.

Place construction membrane on formation and place single sized gravel between the building and the installed drainage channel.

Scaffolding

Erect Scaffolding to allow all works to roof and walls to be undertaken and remove from site on completion of works.

Fascia’s, Soffits and Rainwater goods

Replace all fascia’s, soffits and Rainwater goods with new matching existing as close as is possible and deep flow UPVC guttering securely fixed to fascia and replaced downpipes.

Bell Tower Roof Works

Remove existing roof tiles, temporarily store for reuse, replace or repair construction & roof timbers, install breather membrane & new treated battens, replace tiles stored for reuse with any damaged or missing tiles being replaced and new Lead Flashings.

Chapel Roof Works

Remove existing roof tiles, temporarily store for reuse, replace or repair construction & roof timbers, install breather membrane & new treated battens, replace tiles stored for reuse, any damaged or missing tiles being replaced and new Lead Flashings being installed.

Brickwork and Parapets

Remove all loose mortar and bricks and replace any bricks with matching, point up brickwork where required and re-fix and/or repoint parapet copings.

Floor Works

Break up the existing floor throughout the building, excavate to reduce levels and construct new floor incorporating 1000-gauge D.P.M., a minimum of 100mm depth of Insulation material and a 75mm thick sand/cement floor screed.

Internal Wall Works and Ceiling

Remove existing timber Dado rail and all existing Plaster from walls.

Inject chemical D.P.C. and Tank all walls.

Dryline walls with a Breather Membrane, treated battens and moisture resistant Plasterboard with a Plaster skim finish and fit new skirting boards.

Repair Plaster Ceiling

Doors

Remove all doors, ease, adjust and rehang to new floor level using new hardware.

Glazing Works

Repair and make safe all existing windows and frames

Install new internal secondary double glazing

Electrical Works

Upgrade the existing Electrical Installation to current standards

Decoration Works

Completely decorate all internal walls and both internal and external doors

Decorate all external woodwork and all Cast Iron rainwater goods

Additional Drainage Works

Supply and install a 100mm diameter perforated and flexible Drain in a minimum of 150mm of C20P concrete beneath the existing roadway and connect the proposed drain into the existing land drain adjacent to the pedestrian access to the cemetery utilising a Pre-Formed UPVC chamber.