## Slide 1
Aircraft Wash
Demand for Aircraft Wash issued.
Date and time agreed with contractor. (5 working days notice for booking, 3 days cancellation notice required).
Contractor arrives at site
Wash completed using TO’s
Sqn rep observes wash process
GFx
Water from tap -> hose to wash pan. Anything beyond this point is owned or hired by the contractor.
Sqn provide wash solution.
Stn arrange for the emptying of the wastewater container.
Contractor hires/supplies & uses equipment.
Sqn rep confirms completion of satisfactory wash
A/C prepped and delivered to washpan by 07:30hrs.
Wash can not happen if it’s under 5 degrees.
Sqn - Deprep from wash
Sqn - Post wash lube
Sqn – Approach to remove the requirement for the decision with sqn, and Eng Ops run it to ground if it needs to be cancelled due to weather. Amendment to the AESO.
Colour Key
MoD
Contractor

## Slide 2
Colour Key
MoD
Contractor
Remove wheel assembly from aircraft
Complete MOD Form 731
Demand issued using Form 731 copy
Sqn move the wheel/tyre to building 180
Contractor collects wheel assembly and consumables from B-180 (e.g grease)
Inspection of wheel assembly
Carry out maintenance/repair
If any components are out of limits and need replacing, demand should be placed through the Airseeker DT
If in doubt, contact Airseeker DT for determination on how to proceed
Surface finish as required (no TO reference)
Pass to Contractor Logs (B-180)
GFX
Ring adaptors for RJ
Consumables
Items (greases) provided by 51 Sqn
Sqn collect
Tyres for disposal collected (if req)
Wheel & Tyres

## Slide 3
Prep for Use
Prep Engine for despatch to Sqn
Engine Support
Prep/Deprep Transport
Engine Inhibit every 6 months
Tow the Engine on its stand, Air Start Trolley, Inhibit Rig, Aux trolley and N2 trolley to Wash Pan
Prep Engine for transport as required iaw TO’s
De-prep Engine from Transport
Then either inhibit or use in ac
GFx
Green inhibit rig (XGG 245001)
2 stands
1 sling (U/S) P/N - JMP/OIL/D/7199
Arrange with 51 Sqn
Carry out inhibit in accordance with TO’s
Tow the Engine on its stand, Air Start Trolley, Inhibit Rig, Aux trolley and N2 trolley to Engine Bay.
Colour Key
MoD
Contractor

## Slide 4
Oxygen Support
LOX Support
Decant from 10000l to 200l LOX Trolley
Samples from 200l trolley
Inspect LOX parts for damage. Repair as required, demand parts through iMOPS.
Make available for use
Ad-hoc and regular servicing (Weekly inspection/3/6/12/24mths)
Prep for deployments
Send samples to BOC via F&L
BOC take samples from 10000l tank; contractor escort
LOX trolleys filled everyday, and full on Fri
Call out on demand on weekend but unlikely
Daily reports to Eng Ops
Gaseous O2 Support
Contractor responsible for support to O2 trolley O2 elements.
Ad-hoc and regular servicing (6/12/24mths)
Prep for deployments
GFX
3x LOX Trolleys
3x Gaseous oxygen Trolleys
Colour Key
MoD
Contractor
51Sqn collect trolleys from bay and return
Stn support main trolley and wheels