PART TWO

SPECIFICATION

PREAMBLE

General Requirements

Tenders are invited from Kettering Borough Council for the refurbishment of the chapel at Desborough Cemetery, Rushton Road, Desborough, Northamptonshire NN14 2QB.

Information, Costs and Expenses

Contractors are responsible for obtaining all information necessary for the preparation of their Quotation and all costs expenses and liabilities incurred in connection with the preparation and submission of a quotation.

Submission of Quotation

Your quotation should be submitted together with any Pricing Schedule and Supporting Information to:

webprocurement@kettering.gov.uk.

Further information and Queries

Please address any queries or requests for further information to:

webprocurement@kettering.gov.uk

Freedom of Information Act 2000:

  - Information in relation to this tender may be made available on demand in accordance with the requirements of the Freedom of Information Act 2000.

  - Contractors should state if any of the information supplied by them is confidential or commercially sensitive or should not be disclosed in response to a request for information under the Act.  Contractors should state why they consider the information to be confidential or commercially sensitive.  This will not guarantee that the information will not be disclosed but will be examined in the light of the exemptions provided in the Act.

  - It is important to note that information may be commercially sensitive for a time (e.g. during a tender process) but afterwards it may not be.  The timing of any request for information may be extremely important in determining whether information is exempt.  However, contactors should note that no information is likely to be regarded as exempt forever.

SPECIFICATION

Introduction and Context

The current chapel is in a poor state of repair and is well below current construction standards. The intention is to undertake all the essential repairs to the chapel to maintain its structural integrity and improve its current condition such that further works are not required for a minimum of 5 years. When the work is being executed the successful contractor shall ensure that all areas of the cemetery can be regularly used by funeral directors, visiting public and maintenance contractors.

Core Works

Refurbish roof by installing new breather felt and Flashings, replace existing floor, repair / replace internal finishes and install secondary glazing to existing Chapel at Desborough Town Cemetery, Rushton Road, Desborough, Northamptonshire NN14 2QB.

It is intended to improve the condition of the chapel by:

- Cutting back all overhanging tree branches to leave the remaining branches a minimum of 2.0m distance from the chapel.

- Erecting Scaffolding to undertake roof works and removal on completion.

- Executing roofing works including installation of new breather felt on new treated battens with new Lead Flashing.

- Renewing Cast Iron gutter to rear of chapel.

- Repairing cracked and defective rainwater downpipes.

- Raking out and pointing up stone copings to parapets.

- Repairing existing stonework.

- Removing existing raised Dias and properly dispose of.

- Breaking up existing floors and install new insulated floor with D.P.M and a minimum of 75mm depth of screed.

- Removing all defective plaster, injecting a chemical DPC and tanking to walls, Dry lining walls, finishing walls with plaster skim and installing new skirting boards.

- Easing doors, fitting new hardware and rehanging all internal and external doors.

- Installing secondary double glazing and making repairs to existing glazing

- Completely decorating internal walls, all doors and Rainwater goods to protect completed works.

It is envisaged that there will be a minimum of excavation and it should be noted that the excavated material should be removed from site and properly disposed of.

The area available for construction of the works is the whole of the Cemetery as defined by distinct fenced boundaries and clearly visible on site. Contractors should indicate the intended sites for storage of materials when submitting their tender.

Contractors should indicate the measures that they will take to allow any funerals to be undertaken and the period for which they are likely to be on site.

Responsibilities

The Pubic Services Team is responsible for the maintenance of the grounds, including the excavation of graves, any allocation of plots that maybe required and for these works being executed.

Use of Site

Desborough Town Cemetery is still in use and there is an average of two funeral service per month held at the site. Funeral and Internment of Ashes services are carried out within the cemetery and Contractors should ensure that the site is as clear as is possible of construction materials, plant and staff whilst any services are being executed.

The Bereavement Services Section of the Council will give a minimum of 7 day’s notice of any funeral or other service at Rothwell Town Cemetery to the Project Manager who will notify the successful tenderer during the time of the execution of the work.

OUTLINE SPECIFICATION FOR WORKS AT ROTHWELL TOWN CEMETERY

Site Clearance

Cut back all overhanging tree branches to ensure that there is a minimum of 2 metres clearance between the building and the nearest tree branches and properly dispose of all arisings.

External Works

Clean out all guttering, drainage channels and gullies on completion of works and properly dispose of all arisings.

Scaffolding

Erect Scaffolding to allow all works to roof and walls to be undertaken and remove from site on completion of works.

Fascia’s, Soffits and Rainwater goods

Repair or replace all fascia’s and soffits with any new fascia’s and soffits matching the existing.

Repair or Replace Rainwater goods with new Cast Iron matching the existing.

Clean out, repair and redecorate existing cracked and defective rainwater downpipe.

Chapel Roof Works

Remove existing roof tiles, temporarily store for reuse, replace or repair any damaged roof timbers, install breather membrane & new treated battens, replace tiles stored for reuse with any damaged or missing tiles being replaced and new Lead Flashings being installed.

Parapet Works

Rake out all joints and repoint all parapet stone copings

Brickwork

Repair all existing spalled stonework.

Repair area of badly weathered pointing.

Repair cracks in stonework utilising Hellifix reinforcement ties installed in strict accordance with the manufacturer’s instruction.

Floor Works

Remove existing raised Dias and properly dispose of all arisings.

Break up the existing floor throughout the building, excavate to reduce levels and construct new floor incorporating any hardcore required, 1000-gauge D.P.M., a minimum of 100mm depth of reinforced C30P concrete, a minimum of 100mm depth of Insulation material and a 75mm thick sand/cement floor screed with power float finish.

Internal Wall Works

Remove all defective lime plaster from walls.

Inject chemical D.P.C. and Tank all walls.

Dryline walls with a Breather Membrane, treated battens and moisture resistant Plasterboard with a Plaster skim finish.

Supply and fit new skirting boards.

Doors

Remove both sets of access doors.

Form raised brick threshold incorporating a water bar to suit new floor level.

Cut off base of doors to suit new threshold level and rehang doors.

Glazing Works

Repair and make safe all existing windows and frames

Install new internal secondary double glazing

Decoration Works

Completely decorate all internal walls and both internal and external doors

Decorate all external woodwork and all Cast Iron rainwater goods