## Slide 1: PERFORM: TPWS Overspeed Sensor System (OSS) Setting Optimisation (T1174)
Supplier engagement event

## Slide 2: Project background

## Slide 3: Project background
What triggered this proposal? Following the introduction of new trains with improved braking and acceleration performance operating on several routes on the GB mainline, there has been an apparent increased rate of Train Protection and Warning System (TPWS) Overspeed Sensor System (OSS) trips.
There is a belief that this is because drivers are now driving to the increased performance of the new rolling stock and starting to brake later (compared to the older rolling stock), at a point that would still allow them to comply with company professional driving policies and to stop at the signal, or comply with the reduction in speed. However, this has the result that the train passes the OSS at a higher speed than the OSS is set for and the trainborne TPWS reacts and applies the emergency brake on the train.
Further to increased TPWS OSS trips and driver frustrations, there is also a belief that this is influencing overly cautious defensive driving, which in turn reduces network capacity. In comparison, other systems such as Automatic Train Operation (ATO) can operate safely at a much higher approach speed.
This issue had been raised at the Control Command and Signalling Standards Committee (CCS SC) and Train Control Technical Subgroup (TCTSG). Both groups supported research being undertaken to understand the way the system had been set up in order to inform optimal settings.

## Slide 4: Project objectives

## Slide 5: Project objectives
The objectives of this project are to:
Identify all factors involved in the setting of trainborne TPWS OSS trigger delay timers
Establish the rationale for the selection of alternative timer settings originally intended for different train types, as included in the original TPWS specification
Evaluate the current timer setting for passenger trains against trains with enhanced and reliable braking performance
Evaluate the number of TPWS OSS brake demands and establish whether the introduction of new/modified rolling stock with enhanced and reliable braking (that would stop a train prior to the conflict point; collision with the buffer stops; or adequately reducing speed before reaching a speed restriction) resulted in an increased rate of TPWS OSS brake demands
Establish whether and what alternative trainborne TPWS OSS trigger delay timer settings could be applied to trains with better braking performance, without compromising the overall effectiveness and availability of the whole system or the safety of the railway

## Slide 6: Where does the research fit within industry activities? RSSB research activities
Activity details Activity status
T1169 Review of the Uff-Cullen Recommendations related to train protection systems
Review of current status and applicability of original recommendations
Determination of additional measures that should be taken to mitigate risk from SPADs and overspeeds
Consideration of future implementation activities
T1174 PERFORM: TPWS Overspeed Sensor System (OSS) Setting Optimisation Investigation of what alternative trainborne TPWS OSS trigger delay timer settings could be applied to trains with better braking performance, without compromising the overall effectiveness and availability of the whole system; or the safety of the railway
Evaluation of options for novel train protection technologies
Alternative transferable existing solutions for GB rail
New and/or extended usage of current TPWS system
New approaches to train protection
R### Synthesised RAATS / SORAT tool Feasibility study to develop a tool for providing signal-specific risk assessments, to inform decisions on engineering and operational mitigations to SPAD risk
R### Update to T1043 Viability of European Train Control System limited supervision for GB application
Update T1043 to recognise current GB rail SPAD rates and compare programme status to the original report
In delivery
Start – Jan 2019
Finish – May 2019
Under development
Start – April 2019
Finish - Oct 2019
In delivery
Start – Jan 2019
Finish – Mar 2019
Proposed Initial discussion Jan 2019
Proposed Targeted Initial discussion Feb 2019
Wider industry activities
Development and enhancement of the current TPWS Phase 1
The first phase of the review sets out to assess the viability of high integrity train protection technology options, to simplify industry implementation
The review shall commence in March 2019 with preliminary reports expected by June 2019
The review shall incorporate extensive industry engagement
Development and enhancement of the current TPWS Phase 2
Subject to the findings from Phase 1, a second phase of work may be commissioned to develop and test the selected solution(s)
Development of simple migration strategies from TPWS to ETCS LS
The workstream sets out to undertake a short development programme to aid the migration from TPWS to ETCS Limited Supervision (including both trackside and trainborne options)
Review of the current Digital Railway ETCS plan
The workstream will seek to identify further business benefits that may not yet be recognised from the Digital Railway ETCS plan and the emerging Long-Term Plan
Review of resultant revised risk and business cases
Building upon RSSB research, this workstream will determine signal locations that would most benefit from additional/improved train protection system fitment (considering risk, costs, timescales and other benefits)
Notes: Note:
Red Aspect Approaches to Signals (RAATS)
Signal Overrun Risk Assessment Tool (SORAT)

## Slide 7: Alignment to industry initiatives
This research supports the 'Rail Operations and Variability' workstream, which constitutes part of the Enabling Better Performance Research Challenge (PERFORM). PERFORM sets out to achieve performance improvements to run more trains on time today while improving the rail performance of tomorrow. PERFORM was developed by RSSB and consists of five core workstreams:

## Slide 8: Project scope

## Slide 9: Project scope (1 of 4)
In scope | Out of scope
Establish the rationale for the setting of trainborne TPWS OSS trigger delay timers 974 ms [+/- 2ms] 1218 ms [+/- 2ms] Establish how brake response times influenced the rationale for trigger delay timer settings | Measuring the braking performance of rolling stock
Establish the rationale for the selection of alternative timer settings originally intended for different train types, as included in the original TPWS specification: 791 ms [+/- 2ms] 852 ms [+/- 2ms] 1096 ms [+/- 2ms] 1339 ms [+/- 2ms] 1461 ms [+/- 2ms] 1887 ms [+/- 2ms] Establish how brake response times influenced the rationale for alternative trigger delay timer settings | Principles for route compatibility
Evaluate the passenger train TPWS OSS trigger delay timer setting (974 ms) against: Different capabilities of rolling stock currently in operation on the GB mainline that have a demonstratable emergency braking rate or full service braking rate of 12%g or better* Impact of railhead conditions (coefficient of friction) on achievable braking Brake response time Positioning of OSS arming and trigger loops | Movement of position and configuration of OSS loops on the track
Notes: Note:
*: Assuming ‘good’ adhesion conditions (railhead conditions can significantly impact achievable braking rates)
Railway Group Standard GERT8030 ‘Requirements for a Train Protection and Warning System (TPWS)’ Issue 1 (Issued August 2000) stipulated that:
  ‘If the appropriate trigger frequency is detected before the trigger delay timer reaches the trigger delay time then a maximum available automatic brake application shall immediately be initiated’ (7.2.1.5, PG 10)
  ‘If, before detecting the loss of the arming frequency, the train sub-system detects the presence of the appropriate trigger frequency then a maximum available automatic brake application shall immediately be initiated’ (7.2.2.2, PG 10)
The wording within GERT8030 Issue 2 (Issued August 2004) was changed as follows:
  ‘If the appropriate trigger frequency is detected before the trigger delay timer reaches the trigger delay timer setting then a maximum available, maximum integrity, automatic brake application shall immediately be initiated’ (C4.2, PG 13)
  ‘If, before detecting the loss of the arming frequency, the train sub-system detects the presence of the appropriate trigger frequency then a maximum available, maximum integrity, automatic brake application shall immediately be initiated’ (C4.3, PG 14)
This wording was retained for GERT8030 Issue 3 (Issued April 2010) and GERT8030 Issue 4 (Issued December 2011).
GERT8030 Issue 4 and GERT8035 ‘Automatic Warning System (AWS)’ Issue 2 were combined into GERT8075 ‘AWS and TPWS Interface Requirements’ Issue 1 (Issued September 2013). The wording had been changed as follows:
  ‘If the appropriate trigger frequency is detected before the trigger delay timer reaches the trigger delay timer setting, an emergency brake application, or where available an enhanced emergency brake application, shall immediately be initiated’ (3.2.3.5, PG 29)
  ‘If, before detecting the loss of the arming frequency, the train sub-system detects the presence of the appropriate trigger frequency, an emergency brake application, or where available an enhanced emergency brake application, shall immediately be initiated.’ (3.2.4.2, PG 29)
This change reflected that the ‘maximum integrity’ brake may not be the ‘maximum available’ in terms of braking rate. For instance, the Class 390 (Pendolino) has a full service braking rate of 12%g and an emergency braking rate of 9%g. This is due to the requirement for the emergency brake to be ‘failsafe’ (utilising a pneumatic brake). The architecture of the service brake is not designed as a failsafe system, and regenerative braking (which is used for the service brake) is not applied for emergency braking. There are thought to be other train classes that have a similar set up.
A change to Railway Group Standard GERT8075 would be required if TPWS design were to be based on initiating the maximum available braking rate (as opposed to ‘an emergency brake application, or where available an enhanced emergency brake application’). Any such proposal would require a robust risk evaluation to assess non-failsafe elements of braking systems, which could fail to operate when TPWS demands a brake application. Any such implementation would likely be a significant undertaking.

## Slide 10: Project scope (2 of 4)
In scope | Out of scope
Identify the total number of TPWS OSS brake demands on the GB rail network over 2013 – 2018: Map the total number of TPWS OSS brake demands by: TPWS brake application (approach to signals; approach to buffer stops; speed restrictions) Route Train class Timeline Cause (train, track, driver) | Rolling stock currently in operation that do not have an emergency braking rate or full service braking rate of 12%g or better
Establish on a route by route basis, whether the introduction of new/modified rolling stock with enhanced and reliable braking has resulted in an increased rate of TPWS OSS brake demands. The data should be mapped by: TPWS brake application (approach to signals; approach to buffer stops; speed restrictions) Area Identify ‘hot spots’ (locations) where TPWS OSS brake demands are prevalent Train class Timeline Cause (train, track, driver) Assess the consequential risks and performance impacts of the increased rate of TPWS OSS brake demands Assess the consequential risks and performance impacts if current trainborne TPWS OSS trigger delay timers are to be retained on the GB rail network | 
Notes: Note:
TPWS OSS brake demand incidents are to be sourced from SMIS (Safety Management Intelligence System) and Train Operating Companies (where available)

## Slide 11: Project scope (3 of 4)
In scope | Out of scope
Identify alternative/optimal trainborne TPWS OSS trigger delay timer settings that could be applied to trains with enhanced and reliable braking performance (a demonstratable emergency braking rate or full service braking rate of 12%g or better*). For each alternative timer setting, undertake a technical, performance and risk assessment for each of the following TPWS brake applications, to ensure that alternative settings do not compromise the overall effectiveness and availability of the whole system; or the safety of the railway: Approach to signals Gap in protection speeds between the OSS and the Train Stop System (TSS) [i.e. where the train may exceed the overlap or reach the danger point] Maximum line speed (in relation to the train stopping prior to the conflict point) Maximum attainable speed (in relation to the train stopping prior to the conflict point) Impact of railhead conditions (coefficient of friction) on achievable braking Brake response time TPWS ‘minus’ loops TPWS ‘zero’ loops Main aspect approach release from red (MAR) Level of risk imported by TPWS through current TPWS events Constraint of TPWS on the system and limitations on unlocking capacity Impact of alternative trainborne TPWS OSS trigger delay timer settings on approaches to signals Clarification of potential benefits (for instance, improvement in performance, increase in capacity, reduction in sectional running times, platform reoccupation times, etc.) | 
Notes: Note:
*: Assuming ‘good’ adhesion conditions (railhead conditions can significantly impact achievable braking rates)
‘TPWS minus’ is not an official term and has been applied to an additional OSS loop that may be provided closer to the signal than a ‘standard’ OSS loop (often due to reduced distances to conflict points) in order to manage the risk of a train that is accelerating, typically from a station stop, which starts ahead of the standard OSS loop and could still reach the signal at a speed too high for the TSS to be effective. This limited overlap could potentially be applied at a signal protecting a level crossing adjacent to a station platform, for example, Cosham.
‘TPWS zero’ (also known as ‘OSS (0)’) is not an official nomenclature and has limited application and recognition. ‘TPWS zero’ has been applied to TSS track fitment to prevent shorter formation trains starting further back from a platform starting signal from reaching an attainable speed. Examples include Waterloo station and Gatwick Airport (up direction on Down Fast line).

## Slide 12: Project scope (4 of 4)
In scope | Out of scope
Approach to buffer stops Maximum line speed (in relation to the train stopping prior to the buffer stops) Maximum attainable speed (in relation to the train stopping prior to the buffer stops) Impact of railhead conditions (coefficient of friction) on achievable braking Brake response time Level of risk imported by TPWS through current TPWS events Impact of alternative trainborne TPWS OSS trigger delay timer settings on approach to buffer stops Clarification of potential benefits | 
Speed restrictions Maximum line speed (in relation to the train adequately reducing speed before reaching a speed restriction) Maximum attainable speed (in relation to the train adequately reducing speed before reaching a speed restriction) Impact of railhead conditions (coefficient of friction) on achievable braking Brake response time Level of risk imported by TPWS through current TPWS events Constraint of TPWS on the system and limitations on unlocking capacity Impact of alternative trainborne TPWS OSS trigger delay timer settings on speed restrictions Clarification of potential benefits | 
Acquire and evaluate available data on train braking performance (for rolling stock currently in operation on the GB mainline that have a demonstratable emergency braking rate or full service braking rate of 12%g or better*) | 
Acquire and evaluate available data on TPWS OSS brake demands | 
Notes: Note:
*: Assuming ‘good’ adhesion conditions (railhead conditions can significantly impact achievable braking rates)

## Slide 13: Project delivery plan

## Slide 14: Project delivery plan
Completed
Procure
  Out for tender
  In contract
Deliver
  Start of delivery
  End of delivery
Close
  Publication
    Report
    Research in Brief
Late Feb 19
Mid Apr 19
Late Apr 19
Lat Oct 19
Dec 19
Delivery Subject to RSSB budget approval, the project shall be competitively tendered:
Delivery is estimated at approximately six months
The supplier budget is currently estimated at C. £90k

## Slide 15: Q&A