## Slide 1: South Bank Coke Ovens (SBCO)
Decontamination Project
By Products

## Slide 2
No | Plant item | Dwg No | Dimensions (m) | Substance | Estimated Residue [t] | Substance Locale
1 | Primary Cooler | CO 10493 | 3.8 dia x 24 H | Tar/Naphtha/Nh3 Liquor | 6 + 6 + 6 | Base, Middle & Top stage + shell
2 | Exhausters x 2 | CO6233 | 1 dia | Tar/Naphtha/Nh3 Liquor | 1 | Casing & Turbo blades
3 | Secondary Cooler | CO 9098 | 4 dia x 21 H | Tar/Naphtha/Nh3 Liquor | 6 + 6 | Top stage + Shell
4 | Primary Naphtha plant | N/A | 5 small vessels | Tar/Naphtha/Nh3 Liquor | 3 | Base + Shell
5 | Primary NH3 washer | CO 11568 | 3.5 dia x 30 H | Tar/Naphtha/Nh3 Liquor | 6 + 6 + 6 | Base, Middle & Top stage + shell
6 | Secondary NH3 washer | CO 5036 | 4.87 dia x 42 H | Tar/Naphtha/Nh3 Liquor | 6 + 6 + 6 | Base, Middle & Top stage + shell
7 | No 1 NH3 washer | CO 4349 | 4.87 dia x 42 H | Tar/Naphtha/Nh3 Liquor | 6 + 6 + 6 | Base, Middle & Top stage + shell
8 | No 2 NH3 washer | CO 4349 | 4.87 dia x 42 H | Tar/Naphtha/Nh3 Liquor | 6 + 6 + 6 | Base, Middle & Top stage + shell
9 | No 3 NH3 washer | CO 4349 | 4.87 dia x 42 H | Tar/Naphtha/Nh3 Liquor | 6 + 6 + 6 | Base, Middle & Top stage + shell
10 | No 1 Benzole washer | CO 5035 | 4.57 dia x 38 H | Creosote Oil/Benzole | 15 + 207 | Base, 26 stages + shell residue
11 | No 2 Benzole washer | CO 5035 | 4.57 dia x 38 H | Creosote Oil/Benzole | 15 + 207 | Base, 26 stages + shell residue
12 | No 3 Benzole washer | CO 5039 | 4.57 dia x 38 H | Creosote Oil/Benzole | 15 + 207 | Base, 26 stages + shell residue
13 | No 1 Final Naph washer | CO 295 | 11 x 2.75 x 5.4 | Creosote Oil/Benzole | 41 | Base + Shell
14 | No 2 Final Naph washer | CO 295 | 11 x 2.75 x 5.4 | Creosote Oil/Benzole | 41 | Base + Shell
15 | No 3 Final Naph washer | CO 295 | 11 x 2.75 x 5.4 | Creosote Oil/Benzole | 41 | Base + Shell
16 | No 1 Tar decanter | CO 11571 | 4.5 x 3.3 x 15 | Tar/Naphtha/Nh3 Liquor | 25 | Base, + shell
17 | No 2 Tar decanter | CO 11571 | 4.5 x 3.3 x 15 | Tar/Naphtha/Nh3 Liquor | 25 | Base + shell
18 | Tar pump tank | CO 11564 | 2 dia x 6.5 L | Tar/Naphtha/Nh3 Liquor | 20 | Base, + shell
19 | No 1 Liquor pump tank | CO 11565 | 6 dia x 4 H | Tar/Naphtha/Nh3 Liquor | Clean | Base, + shell
20 | No 2 Liquor pump tank | CO 11565 | 6 dia x 4 H | Tar/Naphtha/Nh3 Liquor | 14 | Base,+ shell
21 | North Tar storage tank | CO 11782 | 4 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 10 | Base cone + shell
22 | South Tar storage tank | CO 11782 | 4 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 10 | Base cone + shell
23 | Virgin liquor tank | CO 11588 | 10 dia x 10 H | Tar/Naphtha/Nh3 Liquor | 10 | Base cone + shell
24 | North Weak Liq tank | N/A | 2.6 dia x 9.5 L | Ind water silt | 1 | Base
25 | South Weak Liq tank | N/A | 2.6 dia x 9.5 L | Ind water silt | 1 | Base
26 | Effluent storage tank No 1 | CO 11830 | 11 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 105 [liq] + 27 [Tar] | Base + shell
27 | Effluent storage tank No 2 | CO 11733 | 11 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 105 [liq] + 29 [Tar] | Base + shell
28 | Effluent storage tank No 3 | CO 11830 | 11 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 105 [liq] + 62 [Tar] | Base + shell
29 | Effluent storage tank No 4 | CO 11830 | 11 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 114 [liq] + 105 [Tar] | Base + shell
SBCO By-product Recovery Plant Decontamination Project
Details & contents of Vessels, Tanks, & Sumps

## Slide 3
No | Plant item | Dwg No | Dimensions (m) | Substance | Estimated Residue [t] | Substance Locale
30 | NWL effluent surge vessel | N/A | 1 dia x 2 H | Tar/Naphtha/Nh3 Liquor | .25 | Base + shell
31 | “L” Tar tank | N/A | 11 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 248 | Base + shell
32 | “M” Tar tank | N/A | 11 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 251 | Base + shell
33 | “N” Tar tank | N/A | 11 dia x 12 H | Tar/Naphtha/Nh3 Liquor | 10 | Base cone + shell
34 | Bz storage tank | CO 10996 | 5 dia x 9.4 H | Benzole sludge | 6 | Base + shell
35 | Bz distillation still [west] | CO10348 | 1.5 dia x 9 H | Creosote Oil/Benzole | 1 | Base + shell
36 | Bz make tank North | CO 3562 | 2.75 dia x 6.1 L | Creosote Oil/Benzole | 11 | Base + shell
37 | Bz make tank South | CO 3562 | 2.75 dia x 6.1 L | Creosote Oil/Benzole | 11 | Base + shell
38 | Bz/Water separator | A95893 | 1 dia x 5 H | Creosote Oil/Benzole | .25 | Base + shell
39 | Bz phlegm oil/water separator | N/A | 1 dia x 6 H | Creosote Oil/Benzole | .25 | Base + shell
40 | Bz primary foul water tank | A116907 | 2.7 dia x 3 L | Creosote Oil/Benzole | 1.5 | Base + shell
41 | Bz secondary foul water tank | CO11556 | 2 dia x 6.5 L | Creosote Oil/Benzole | .75 | Base + shell
42 | Bz oil buffer tank | N/A | 2 dia x 5 L | Creosote Oil/Benzole | 6 | Base + shell
43 | Bz reclaim oil tank | N/A | 2 dia x 5 L | Creosote Oil/Benzole | 1.5 | Base + shell
44 | Bz make tanks Annulus pot | N/A | 1 dia x 2 H | Mineral Oil | .25 | Base + shell
45 | East Debenzolised oil tank | CO4533 | 2.7 dia x 9 L | Creosote Oil/Benzole | 36 | Base + shell
46 | West Debenzolised oil tank | CO4533 | 2.7 dia x 9 L | Creosote Oil/Benzole | 36 | Base + shell
47 | Bz Rich Oil heater No 3 | CO4088 | 1 dia x 6 H | Creosote Oil/Benzole | .5 | Base + shell
48 | Bz Rich Oil heater No 4 | CO4088 | 1 dia x 6 H | Creosote Oil/Benzole | .5 | Base + shell
49 | Bz Oil/Oil heat exchrs x 13 | CO4077 | 0.23 dia x 5 L | Creosote Oil/Benzole | 2.6 | Shell & Tube
50 | Bz Oil/Vapour heat exchrs x 2 | CO3554 | 0.7 dia x 3.5 L | Creosote Oil/Benzole | .4 | Shell & Tube
51 | Bz Dephlegmator | CO3554 | 0.7 dia x 3.5 L | Creosote Oil/Benzole | .2 | Shell & Tube
52 | Bz condensers x 2 | CO3554 | 0.7 dia x 3.5 L | Creosote Oil/Benzole | .4 | Shell & Tube
53 | Bz regen vessel | N/A | 0.7 dia x 3 L | Creosote Oil/Benzole | 1 | Base + shell
54 | Bz oil plate coolers x 2 | N/A | 2 H x .3 W | Creosote Oil/Benzole | .5 | Plates
55 | Bz spiral oil cooler | N/A | 1 dia | Creosote Oil/Benzole | 1 | Shell
56 | Bz storage tank drain pot | N/A | 1 dia x 2 L | Creosote Oil/Benzole | .25 | Base + shell
57 | Coal oiling tank | N/A | 2.6 dia x 7.7 L | Processed Fuel Oil | .25 | Base + shell
58 | Boiler plant HFO tank | N/A | 3 dia x 10 H | Heavy Fuel Oil | 43 | Base + shell
SBCO By-product Recovery Plant Decontamination Project
Details & contents of Vessels, Tanks, & Sumps

## Slide 4
No | Plant item | Dwg No | Dimensions (m) | Substance | Estimated Residue [t] | Substance Locale
59 | Boiler plant Hot well tank | N/A | 2 x 2 x 4 | Industrial water silt | 1 | Base
60 | Boiler plant Blow Down Tank | N/A | 2 x 2 x 4 | Industrial water silt | 1 | Base
61 | Gas holder | CO 10176 | 41 dia x 74 H | Gasholder sealant | Solids removed | Piston + shell
62 | Gasholder oil storage tanks x 2 | N/A | 1 dia x 2 L | Gasholder sealant | Solids removed | Base + shell
63 | Gasholder oil pump tanks x 3 | N/A | 1 x 1 x 4 | Gasholder sealant | Solids removed | Base + shell
64 | Wagon shop diesel tank | N/A | 3 dia x 4 H | Diesel oil | Solids removed | Base + shell
65 | Silicate tank East battery square | N/A | 3 dia x 4 H | Sodium Silicate | 14 | Base + shell
66 | Bz plant firefighting water tank | N/A | 11 dia x 12 H | Industrial water silt | 5 | Base
67 | Bunker hydrant water tank | N/A | 3 x 3 x 4 | Industrial water silt | 12 | Base
68 | Neckar 1o water filter vessel | N/A | 3 dia x 2 H | Industrial water silt | 7 | Base
69 | Simons quencher header tank | N/A | 3 dia x 2 H | Industrial water silt | 7 | Base
70 | Exhauster bearings oil tanks | N/A | 1 x 1 x 1 | Mineral lube oil | .2 | Base + shell
71 | COG main condensate pots x 15 | N/A | 1 dia x 1 H | Tar/Naphtha/Nh3 Liquor | 3.5 | Base + shell
72 | Primary heat exchangers x 8 | N/A | 1.5 dia x9 L | Tar/Naphtha/Nh3 Liquor | 8 | Shell & Tubes
73 | 20 cooler heat exchanger x 1 | N/A | 1.5 dia x 4 | Tar/Naphtha/Nh3 Liquor | 2 | Shell & Tubes
74 | East Low Level Pond | CO 4264 | 12 x 3.6 x 2.6 | Tar/Naphtha/Nh3 Liquor | 112 | Base + Walls
75 | West Low Level Pond | CO 4264 | 12 x 3.6 x 2.6 | Tar/Naphtha/Nh3 Liquor | 112 | Base + Walls
76 | Benzole plant drains pit | N/A | 7.5 x 21 x 1.4 | Creosote Oil/Bz/lNh3 Liquor | 221 | Base + wall
77 | Debenzolised oil tank pit | N/A | 9 x 12 x 1.2 | Creosote Oil/Benzole | 130 | Base + wall
78 | Blow down pit | N/A | 3.6 x 8 x 2.5 | Creosote Oil/Benzole | 72 | Base + wall
79 | Primary Naphtha Pit | N/A | 11 x 8 x 2.5 | Tar/Naphtha/Nh3 Liquor | 220 | Base + wall
80 | Effluent Pit | CO5287A | 11 x 8 x 2.5 | Tar/Naphtha/Nh3 Liquor | 220 | Base + wall
81 | Tar pump house sump | N/A | 3 x 2 x 2 | Tar/Naphtha/Nh3 Liquor | 12 | Base + wall
82 | COG Booster drain pit | N/A | 3 x 2 x 1 | Nh3 Liquor | 0 | Base + wall
83 | Primary cooler sump | N/A | 3 x 2 x 1.1 | Tar/Naphtha/Nh3 Liquor | 9 | Base + wall
84 | East interceptor | N/A | 4.7 x 2 x 2.7 | Tar/Naphtha/Nh3 Liquor | 25 | Base + wall
85 | West interceptor | N/A | 6 x 2 x 1.4 | Tar/Naphtha/Nh3 Liquor | 17 | Base + wall
86 | Ex & 20 cooler drains tanks x 2 | N/A | 1 x 1 x 1 | Tar/Naphtha/Nh3 Liquor | 6 | Base + shell
87 | Nh3 washer water heater | N/A | 1.5 dia x 6 H | Industrial water silt | Cleaned | Base + shell residue
SBCO By-product Recovery Plant Decontamination Project
Details & contents of Vessels, Tanks, & Sumps

## Slide 5
No | Plant item | Dwg No | Dimensions (m) | Substance | Estimated Residue [t] | Substance Locale
88 | BOC N2 cryogen tank | N/A | 5 dia x 7 H | Liquid Nitrogen | Cleaned | Base + shell residue
89 | BOC N2 cryogen vaporisers x 3 | N/A | 1 x 3 x 2 | Liquid Nitrogen | Cleaned | Base + shell residue
90 | BOC N2 cryogen condensers x 5 | N/A | 2 dia x 3 H | Liquid Nitrogen | Cleaned | Base + shell residue
91 | Plant air receivers x 2 | N/A | 1 dia x 3 H | Air /Water | Cleaned | Base + shell residue
92 | Plant Air dryers x 3 | N/A | 1 dia x 3 H | Air/water | Cleaned | Base + shell residue
93 | Gullies | X- 88627a |  | Tar/Naphtha/Nh3 Liquor | 375 solids + 1125 liquor | Base + wall
SBCO By-product Recovery Plant Decontamination Project
Details & contents of Vessels, Tanks, & Sumps
Gullies estimate based on:
2000m L x 1m W x 0.75m D = 1500m3
Split : 25% Residue + 75% Liquor
Item no. | Estimated Residue [t]
1 - 29 | 1,669
30 - 56 | 628
57 - 82 | 1,203
83 - 92 | 58
93 [Gullies] | 375
Coal Tar Mix | 5,250
TOTAL | 9,183

## Slide 6
Benzole Plant
Items 35-55 inc
1
2
3
4
5
6
7
8
9
11
10
13
12
14
15
17
16
18
21
20
19
23
22
25
24
26
27
28
29
30
31
32
33
56
34
57
58
60
59
61
62
63
64
65
66
67
68
69
70
71
72
73
74
75
76
77
78
80
79
81
82
83
84
85
86
87
88
89
90
91
92
93
Location of Process Vessels, Tanks & Sumps
71
71
71
71
SBCO By-product Recovery Plant Decontamination Project

## Slide 7
Coke Oven Gas cleaning by product recovery vessels
SBCO By-product Recovery Plant Decontamination Project

## Slide 8
Benzole washers
Coke Oven Gas cleaning by product recovery vessels
SBCO By-product Recovery Plant Decontamination Project
### Due to the Occupational health risks associated with cleaning out Benzole washers, would recommend
they are laid down on the floor and cold cut into smaller sections prior to cleaning ###

## Slide 9
SBCO By-product Recovery Plant Decontamination Project
Primary Coke Oven Gas Cooler

## Slide 10
SBCO By-product Recovery Plant Decontamination Project
Base of Primary Coke Oven Gas Cooler

## Slide 11
SBCO By-product Recovery Plant Decontamination Project
Secondary Coke Oven Gas Cooler

## Slide 12
Naphthalene Washers
SBCO By-product Recovery Plant Decontamination Project

## Slide 13
Benzole Distillation Plant
SBCO By-product Recovery Plant Decontamination Project
Oil
regenerator
Benzole Rich
Oil Heaters
East
Distillation column
(Still)
Reclaim oil tank
West
Distillation column
(Still)
Oil to Oil heaters
Crude Benzole /Water separator
Oil to Oil Vapour Coolers
Distillation columns
Depghlegmator
Condensers

## Slide 14
Primary COG Cooler Shell/Tube Heat Exchangers
SBCO By-product Recovery Plant Decontamination Project

## Slide 15
Primary COG Cooler Shell/Tube Heat Exchangers
SBCO By-product Recovery Plant Decontamination Project

## Slide 16
Coal Tar & Nh3 Liquor Tanks
SBCO By-product Recovery Plant Decontamination Project

## Slide 17
Heavy Fuel Oil Tank
SBCO By-product Recovery Plant Decontamination Project

## Slide 18
Crude Benzole Tank
SBCO By-product Recovery Plant Decontamination Project

## Slide 19
Crude Benzole Tank
SBCO By-product Recovery Plant Decontamination Project

## Slide 20
Coal Tar & Nh3 Liquor Tanks
SBCO By-product Recovery Plant Decontamination Project

## Slide 21
Coal Tar & Nh3 Liquor Tanks
SBCO By-product Recovery Plant Decontamination Project

## Slide 22
Nh3 Liquor Tanks
SBCO By-product Recovery Plant Decontamination Project

## Slide 23
Benzole Plant Make Tanks
SBCO By-product Recovery Plant Decontamination Project

## Slide 24
Benzole Plant Secondary Water Tank
SBCO By-product Recovery Plant Decontamination Project

## Slide 25
Tar Decant Tanks
SBCO By-product Recovery Plant Decontamination Project

## Slide 26
Tar Make Tank
SBCO By-product Recovery Plant Decontamination Project

## Slide 27
Nh3 liquor Tank
SBCO By-product Recovery Plant Decontamination Project

## Slide 28
Gas Holder Sealant Tanks
SBCO By-product Recovery Plant Decontamination Project

## Slide 29
Diesel Oil Tank
SBCO By-product Recovery Plant Decontamination Project

## Slide 30
Coke Oven Gas cleaning by product recovery sumps
SBCO By-product Recovery Plant Decontamination Project
Debenzolised Oil Pit
Low Level ponds
Effluent Pit

## Slide 31
Debenzolised Oil Pit
Coke Oven Gas cleaning by product recovery sumps
SBCO By-product Recovery Plant Decontamination Project